## Slide 1: Grid-based Cyclic Multi-robot Allocation for Object Carrying
Jee Hwan Park
School of Mechanical Engineering
07/24/2020

## Slide 2: Content
Grid based Cyclic Multi-robot Allocation for object carrying
Introduction
Related Works
Problem Statement
Proposed Solution
Validation
Conclusion & Future works

## Slide 3: Introduction
Background
Object transportation using multi-robot systems has been a popular research topic due to its robustness and fault tolerant feature.
Traditional methods of object transportations are Pushing, Grasping and Caging.
Pushing mechanism
Grasping mechanism
Caging mechanism

## Slide 4: Introduction
Problems statement
Introduced strategies still have some limitations and possible improvable points as follows:
  The strategy can be limited based on the weight of the object
  Requires robots’ functionalities such as grasping
  Alignment of the robot has to be precise to translate the object in desired path

## Slide 5: Introduction
Motivation
What can be a possible way to reduce limitations?
Development of idea of object transportation

## Slide 6: Introduction
Motivation
New method of object transportation using multi-robot system.
  Multi-robot system contains group of spherical robots
  The transition is caused by the rotation of spherical robots
  To maintain the stability while moving, the formation of the robot needs to be designed
3-D Concept of object carrying using multi-spherical robots

## Slide 7: Introduction
Research Question
What is the most efficient allocation strategy to ensure the stability of the object during the transportation while using minimum number of robot required?

## Slide 8: Introduction
Grid-based Cyclic multi-Robot Allocation
The object carrying strategy can use Grid-based Cyclic multi-Robot Allocation (GCRA) method to transport the object maintaining the stability
GCRA method generates the required properties of the grid consisting the information of horizontal gap, and vertical gap,
Grid is generated based on object’s shape and center of mass.
Grid generation concept

## Slide 9: Introduction
Assumptions
This thesis has following assumptions:
  The system is centralized and position of each robot and the object is known. Each robot has accessibility of the object and other robot's position.
  The object has a point contact and there is no slip between the object and the robots.
  The object has a flat surface on the contact with robots.

## Slide 10: Related Works
Pushing, Grasping and Caging strategies

## Slide 11: Related Works
Pushing strategy
Pushing strategy is the methods of using multi-robots that are not attached to the object.
Multi-robots exerts pushing forces on the object to overcome frictional force, gravitational force and other dynamical force during the transportation.
The pushing strategy may appear to be simple but this strategy has challenge of alignment of the total force created by each robots.

## Slide 12: Related Works
Pushing strategy
A strategy for transporting tall objects with a swarm of miniature mobile robots
  Uses swarm of mobile robots to push the object to the desired goal.
  Finite state machine is designed and each robot relocates to push the object.
  Each robot has 8 proximity sensors to detect the object and one color sensor to detect the object and the goal.
Pushing application by Chen and Gauci

## Slide 13: Related Works
Grasping strategy
Grasping strategy transports object by a robot that is physically attached to an object.
Strategy can be accomplished using robots with the grasping mechanism such as robotic arms.
grasping strategy provides a better control of the object once it is grasped and lifted.
Re-positioning of the object using this mechanism is dependent on the weight of the object

## Slide 14: Related Works
Grasping strategy
Kinematic multi-robot manipulation with no communication using force feedback
  The application introduces a multi-robot system to transport an object using a group of four robots.
  The leading robot pulls the object and perceives the direction towards the goal and other three robots pushes the object to produce enough force.
  The control model requires information beforehand such as mass of the object, friction coefficients and total number of the robots forming the group.
Grasping application by Wang and Schwager

## Slide 15: Related Works
Caging strategy
Caging strategy intentionally encloses the object by group of robots and ensures that the object follows the planned trajectories.
From the start of the transportation to the end, the object will be surrounded to avoid any desertion from the enclosure.
The main challenge of the strategy is the allocation and positioning of robots.

## Slide 16: Related Works
Caging strategy
Multirobot Object Transport via Robust Caging
  The control algorithm to collectively transport an object using a group of relatively low-cost robots
  Uses the quality of complete robustness to first optimize the number of robots in the initial formation, and then reorient and move the formation.
  The method is free of force analysis and therefore less prone to sensor errors and failures.
Grasping application by Weiwei and Boxin

## Slide 17: Problem Statement
Mathematical problem statement and Definitions

## Slide 18: Problem statement
Object define
For Grid based Cyclic Robot Allocation (GCRA) method, the object is handled in two dimensional space.
Let the object to be defined as an arbitrary planar shape consisting of the set of boundary points.
the mass of the object is equally distributed and the planar shape 𝑪 is consistent in such that is always with in the boundary of 𝑪

## Slide 19: Problem statement
Grid define
Based on the object’s properties (COM and shape), the grid is generated.
Grid properties includes horizontal gap, and vertical gap,
Robots are located at the cross points of the grid.
Robots are divided in two group, set and set
Stable condition
Unstable condition

## Slide 20: Problem statement
Stability define
As robots travels in velocity, , travels twice faster than that of robots, .
Causes lost of contact of set
Possibility of instability of object and leads to failure of transportation.
Definition of stability needs to be set.
Stable condition
Unstable condition

## Slide 21: Problem statement
Definition 1
Object of uniform weight distribution being carried by spherical robots forming a convex hull is stable, if the geometric centroid of object is always bounded within the convex hull .

## Slide 22: Problem statement
Objective definition
Determine the grid spacing parameters and for the grid formation based on the properties of the object.
Determine the minimum number of robots required denoted as , such that stable omni-directional transportation of the object defined as planar shape with constant and is achieved based on the stability criterion defined in Definition 1.

## Slide 23: Proposed Solution
Grid generation, Robot allocation and Definition 2

## Slide 24: Proposed Solution
Grid generation
With defined object , compute the shortest distance between the center of the mass, and and define it as .

## Slide 25: Proposed Solution
Grid generation
With defined object , set of distances between , needs to be computed first.
Then, compute , where element of is equal to .

## Slide 26: Proposed Solution
Grid generation
With defined computed , define by calculating the shortest distance from line to the .
The minimum element of is then confirmed as .
)

## Slide 27: Proposed Solution
Grid generation, exceptional case
For the exceptional case where every elements of is equal, such as circular shape, the grid gaps are compared and the smaller gap is used for both horizontal and vertical grid spacing.
This makes the required number of robot larger but ensures the stability of the object

## Slide 28: Proposed Solution
Grid generation
With computed properties of the grid, the grid will look as shown below.
Before moving on, we assume that the weight of the object is heavy enough to generate the friction and no-slip condition is satisfied.
In reality, safety margin, and is added.

## Slide 29: Proposed Solution
Robot allocation
The possible positions of the robots to ensure the stability of the object are all the grid intersections.
Setrobots has direct relations of the speed to the speed of the translation.
Extra robots are allocated in every direction on the grid to surround the set and these groups are set .

## Slide 30: Proposed Solution
Robot allocation
The possible positions of the robots to ensure the stability of the object are all the grid intersections.
Setrobots has direct relations of the speed to the speed of the translation.
Extra robots are allocated in every direction on the grid to surround the set and these groups are set .

## Slide 31: Proposed Solution
Definition 2
At any given time all robots in must have eight neighboring robots; two along , two along and four at and diagonal locations from its current position on the grid. The layer of robots fulfilling this requirement and not in set allows omni-directional translation of and constitutes robots of set .

## Slide 32: Validation
Matlab simulation, Result and discussion

## Slide 33: Validation
Hardware
To physically validate the proposed solution, multi-robot system consisting spherical robot is needed. The ideal option for the robot is Sphero.
The economical robot consists multiple sensors such as accelerometer, gyroscope, compass, infrared receiver, infrared emitter, ambient light sensor and motor encoder.
Infrared receiver and emitter, accelerometer and gyroscope can be used to extend the multi-robot system to de-centralized system and autonomous system.

## Slide 34: Validation
Simulation setup
Preparing multiple Sphero is not the most economical way to validate the proposed solution at current state.
Instead of validating the solution physically, simulation was performed. The simulation should satisfy stated definition 1 and definition 2.
For validation, 4 different objects are used:
  Triangular shape () – general solution
  Rectangular shape () – general solution
  Arbitrary shape () – general solution
  Circular shape () – exceptional solution

## Slide 35: Validation
Grid generation simulation
Using the simulation to compute and for .
It followed the stated proposed solution using Matlab.
Same method is applied to the other objects.
Define the object
Compute
Define and
Compute
, = 111.23

## Slide 36: Validation
Grid generation simulation
Same method is applied to the other objects.
Grid is dynamic with speed of robot and the simulation shows the relative grid.
C1 (Triangular shape):
C2 (Rectangular shape):
C3 (Arbitrary shape):
C4 (Circular shape):

## Slide 37: Validation
Robot allocation
Starting location of robots for 4 objects:
C1 (Triangular shape):
C2 (Rectangular shape):
C3 (Arbitrary shape):
C4 (Circular shape):

## Slide 38: Validation
Simulation Result
Object transportation of C3

## Slide 39: Validation
Result
C1 transportation result
C3 transportation result
C2 transportation result
C4 transportation result

## Slide 40: Conclusion & Future Works
Matlab simulation, Result and discussion

## Slide 41: Conclusion & Future works
Conclusion
In this thesis, innovative method of transporting an object is introduced and to efficiently transport the object, Grid-based Cyclic Robot Allocation (GCRA) method is introduced.
The proposed solution was to generate a grid to compute allocation of the robots and the solution was validated using Matlab simulation.
The proposed object carrying method using a multi-robot system of spherical robots can be investigated further on cost and feasibility analysis depending on robot design.

## Slide 42: Conclusion & Future works
Future Works
With successful multi-robot allocation, further work on developing multi-robot formation control will be studied and applied.
With the successful development of the control system, the validation can be extended to the real-life experiment or 3-dimensional simulation environment.

## Slide 43: Thank You.
Jee Hwan Park
765 479 2539
park458@purdue.edu